## Slide 1
MSc ROBOTICS · CASE STUDY · TH DEGGENDORF
EEG-Based Brain–Computer Interface for Assistive Robotic Arm Control
A non-invasive system that turns imagined movement into real robot motion — decoding motor-imagery EEG with CSP + SVM and driving a UR5e manipulator in ROS 2 / Gazebo.
Team Prajwal Dikonda · Nishant Shetty · Papiha Dhavan
Supervisor Prof. Dr.-Ing. Hamidreza Heidari
Analytical review — with independently reproduced results and an honest critique
Notes: Welcome. This is a review of our EEG-BCI project, but with something extra: I re-ran the real training myself, so the results here are verified, and I'll be honest about where the reports run ahead of the code.

## Slide 2
What we'll walk through
01
The problem & why it matters
Who this helps, and the goals we set ourselves
02
How a brain talks to a machine
BCIs, motor imagery, and the EEG rhythms we ride on
03
What the literature taught us
20 papers, and the five gaps that shaped our design
04
The system, end to end
Architecture, dataset, signal processing, features
05
Decoding & moving the arm
SVM classification, ROS 2, MoveIt 2 and Gazebo
06
Does it actually work?
Reproduced accuracy and an honest KPI scorecard
07
Where it falls short
Doc-vs-code gaps, data leakage, unmeasured latency
08
How we'd take it further
Concrete fixes and a research roadmap
Notes: Here's the shape of the talk — from the human problem, through how the system works, to whether it delivers and how we'd improve it.

## Slide 3
Why this project matters
Every year, stroke alone changes millions of lives — and the mind is usually still fully there.
15M
strokes worldwide, every single year
~5M
survivors left with permanent disability
100%
of them keep their cognition — the intent is intact
Here's the heart of it: someone can know exactly what they want to do — reach for a glass, press a button — and simply have no muscular pathway left to do it. A Brain–Computer Interface listens to the brain directly and hands that intention to a robot arm, giving back a slice of everyday independence. The catch we set out to solve: most systems that do this need costly lab hardware, long calibration, and heavy compute.
02
Notes: The stakes are personal. Cognition intact, body unable to follow. A BCI restores the link — and our whole design is about making that link affordable and deployable.

## Slide 4
What we set out to achieve
Our objectives
→
Build a motor-imagery decoding pipeline that's genuinely modular — every stage swappable
→
Choose methods that are light enough to run in real time on an ordinary laptop, no GPU
→
Prove the whole thing in simulation first, before anything touches real hardware
→
Turn decoded thoughts into 4–5 practical arm commands
→
Anchor every single design choice to something in the literature, not a hunch
How we'd know it worked
≥ 75%
Classification accuracy the model should clearly beat guessing
≤ 500 ms
End-to-end latency fast enough to feel connected to the arm
≥ 80%
Command success rate commands land reliably, not occasionally
4–5
Distinct arm movements enough vocabulary to be useful
03
Notes: Five objectives, four numbers to hit. Each KPI isn't arbitrary — they trace back to benchmarks in Lotte 2018, Blankertz 2007 and Abiri 2019.

## Slide 5
How a brain talks to a machine
What a BCI actually is. Think of it as a translator. It reads the brain's electrical activity, works out what the person intends, and passes that on as a command — no nerves or muscles in the loop at all.
Why we read from the scalp. You can tap the brain three ways — and it's a trade-off between signal quality and how invasive you're willing to be.
Invasive
Electrodes implanted in cortex
Sharpest signal — but surgery, and real risk
Semi-invasive
ECoG on the brain's surface
Strong signal, still needs an operation
Non-invasive — EEG
Sensors sit on the scalp
Safe, cheap, portable. Our choice.
04
Notes: A BCI is a translator from intention to command. We use non-invasive EEG — noisier than implants, but safe, affordable and the standard for assistive work.

## Slide 6
The trick: imagined movement
Here's the neat part. You don't have to move at all. Just vividly imagining moving your left hand lights up the sensorimotor cortex in a specific, repeatable way — the brain rehearses the action even when the muscles stay still.
→
ERD — during the imagined move, rhythmic power drops.
→
ERS — once you stop, it rebounds back up.
→
These swings live in the alpha & beta bands — and they're different enough between actions to tell apart.
What the cortex does
Imagine LEFT hand
→ ERD over the RIGHT cortex
Imagine RIGHT hand
→ ERD over the LEFT cortex
Imagine feet
→ desynchronisation at the midline
The EEG rhythms — and the two that matter to us
Band | Range | What it reflects
Delta | 0.5–4 Hz | Deep sleep
Theta | 4–8 Hz | Drowsiness
Alpha | 8–13 Hz | Relaxed — carries MI (ERD)
Beta | 13–30 Hz | Active focus — carries MI (ERS)
Gamma | >30 Hz | High-level processing
Everything downstream — filtering, features, the classifier — is tuned to the 8–30 Hz window where motor imagery lives.
05
Notes: Motor imagery gives us repeatable ERD/ERS signatures in alpha and beta. That 8–30 Hz band is the target for the whole pipeline.

## Slide 7
What the literature taught us
We read 20 peer-reviewed works (2000–2025). Six of them did the most to shape our thinking.
1
Wolpaw et al. (2002)
The founding proof that EEG can drive devices in real time.
→ So motor imagery is a solid basis to build on
2
Pfurtscheller & da Silva (1999)
Pinned down the ERD/ERS neurophysiology.
→ Tells us which bands to trust
3
Ramoser et al. (2000)
Introduced CSP spatial filtering.
→ Became our main feature method
4
Lotte et al. (2018)
10-year review: SVM shines on small datasets.
→ Why we chose SVM
5
Roy et al. (2019)
Deep learning is powerful — but data- and compute-hungry.
→ Why we didn't go deep (yet)
6
Blankertz et al. (2007)
Single short epochs are enough to classify.
→ Makes the 500 ms goal realistic
06
Notes: Six anchor papers. The point isn't the citations — it's that every one maps to a decision we made.

## Slide 8
Choosing the classifier
We compared the field honestly — accuracy is only half the story when you need real-time control.
Approach | Type | Typical accuracy | Compute | Real-time?
SVM (RBF kernel) | Classical ML | 75–85% | Low | Excellent
Logistic Regression | Classical ML | 70–80% | Very low | Excellent
LDA | Classical ML | 70–78% | Very low | Excellent
CNN | Deep learning | 80–90% | High | Moderate
RNN / LSTM | Deep learning | 78–88% | Very high | Poor
Riemannian geometry | Geometric ML | 80–87% | Moderate | Good
Our call
SVM with an RBF kernel wins on fit, not just score.
→
Strong on the small datasets EEG actually gives you
→
Fast enough for real-time control
→
No GPU — runs on a normal laptop
→
Deep learning parked for later: too hungry for now
07
Notes: Deep nets edge out on raw accuracy, but they need data and GPUs we don't have. For this scope, SVM is simply the smarter fit.

## Slide 9
The five gaps we tried to close
Reading the field, the same shortcomings kept coming up. Each one pointed straight at a design decision.
GAP 1
Everyone leans on expensive lab hardware
→ We use free, public datasets instead
GAP 2
Simulation validation is often skipped
→ We validate the whole thing in sim, documented
GAP 3
Systems are welded together, hard to change
→ We built independent, swappable ROS 2 modules
GAP 4
Latency is rarely actually reported
→ We set out to measure it against 500 ms
GAP 5
Most demos manage only 2–3 commands
→ We aim for 4–5 useful directions
08
Notes: Five recurring gaps, five deliberate responses. This mapping is the backbone of our justification.

## Slide 10
The system, end to end
EEG → filtering → CSP → SVM → ROS 2 / MoveIt 2 → Gazebo (UR5e). Five stages, each one testable on its own.
1
EEG input
A public BCI IV-2a recording — 22 channels at 250 Hz
→
2
Preprocessing
Band-pass to 8–30 Hz, then cut into 0–4 s epochs
→
3
Features
CSP finds the spatial patterns that separate classes
→
4
Classify
SVM decides — and only speaks up when it's confident
→
5
Command
The label becomes a robot pose, sent over ROS 2
→
6
Move
MoveIt 2 plans it; the UR5e executes in Gazebo
Because the stages are independent, any one can be upgraded without rebuilding the rest — that's the modularity gap answered directly.
09
Notes: The core architecture. A heads-up for later: in the final code the feature path is CSP only — the ICA and PSD stages are described but not wired in.

## Slide 11
The data we learned from
BCI Competition IV — Dataset 2a. The most-used motor-imagery benchmark there is.
4
classes
left hand · right hand · feet · tongue
22
channels
EEG, plus 3 EOG for artefacts
250 Hz
sampling
fine enough for MI rhythms
9
subjects
288 trials each per session
Why this one
→
It's the field's common yardstick — so our numbers can be compared to everyone else's
→
Every trial is cleanly labelled, which makes supervised training and cross-validation straightforward
→
It's public and standardised — full reproducibility, and it sidesteps the pricey-hardware gap entirely
One honest caveat
The final code actually trains and tests on just one subject (A01). Cross-subject generalisation is described in the report, but it isn't implemented — so the numbers are single-person.
10
Notes: A strong, standard benchmark. But be clear-eyed: only subject A01 is used in the code, so results are single-subject.

## Slide 12
Cleaning the signal
Raw EEG is tiny (10–100 µV) and swamped by blinks, muscle twitches and mains hum. Here's the gap between the plan and the code.
What the report describes
✓
Butterworth band-pass, 8–30 Hz — keeps the MI rhythms
✓
50 Hz notch filter — kills mains hum
✓
ICA artefact removal — strips out eye & muscle noise
✓
±100 µV epoch rejection — drops the ugliest segments
✓
Epoch segmentation, 2–4 s — locked to the imagery cue
✓
Per-channel normalisation — evens out drift
What the code actually runs
✓
Band-pass 8–30 Hz — done
✓
Epoching 0–4 s — done
✗
Notch filter — not in the run path
✗
ICA removal — not in the run path
✗
±100 µV rejection — not in the run path
✗
Normalisation — not in the run path
So in practice, only the band-pass and epoching happen. The richer cleaning is written up but never actually wired in — the first of several gaps we'll come back to.
11
Notes: This is the first honesty slide. The documented pipeline is rich; the executed one is band-pass plus epoching. Worth being upfront about.

## Slide 13
Making the decision — safely
The SVM decides which movement was imagined. But a good BCI also knows when to stay quiet.
The SVM, in plain terms
It draws the widest possible boundary between classes, and the RBF kernel lets that boundary curve — so it can separate patterns that aren't neatly linear.
K(xᵢ,xⱼ) = exp(−γ ‖xᵢ − xⱼ‖²)
→
Four classes handled one-vs-rest, with probability estimates
→
CSP and SVM live in one scikit-learn pipeline — so no test data ever leaks into training
→
Robust on little data, GPU-free, quick to answer
The safety catch
Not every guess deserves to move a robot. We only act on confident ones.
if P(class) ≥ 0.70 → move else → hold still (treat as Rest)
→
Ambiguous epochs get ignored, not acted on
→
Threshold is 0.70 in the final node (the reports say 0.65 — a small inconsistency)
→
Backed by a 2.5 s cooldown and duplicate-command suppression
13
Notes: SVM in a leakage-safe pipeline, plus a confidence gate and cooldown so a shaky read never jerks the arm.

## Slide 14
From command to motion
Three small ROS 2 programs pass the baton: one decodes, one translates to a pose, one makes the arm move.
1
EEG Predictor loads the model, publishes /eeg_command
2
Robot Controller turns a command into a UR5e joint pose
3
MoveIt 2 + Gazebo plans the path and executes it safely
What each imagined action does
Imagined (event) | Command | The UR5e…
Left hand (769) | LEFT | rotates its base left
Right hand (770) | RIGHT | rotates its base right
Feet (771) | FORWARD | reaches forward
Tongue (772) | HOME | returns to its home pose
Why UR5e + Gazebo
A real 6-DOF arm with native ROS 2 and MoveIt 2 support, in a physics simulator with proper collision checking. Best of all: a misread command in sim can't hurt anyone.
14
Notes: A genuinely working ROS 2 / MoveIt 2 / Gazebo stack driving a UR5e. Note the sim platform migrated from PyBullet in the early phase to Gazebo in the final one.

## Slide 15
And plenty that's genuinely strong
For all the caveats, this project earns real credit where it counts.
✓ Grounded in the literature
20 correctly-cited works, and every design choice traces to a source or a gap.
✓ The core result is verified
CSP + SVM really does hit ~75% cross-validated on a standard benchmark.
✓ It's a real, working system
A functioning ROS 2 / MoveIt 2 / Gazebo stack driving a UR5e — not just slides.
✓ Clean ML hygiene
CSP sits inside the scikit-learn pipeline, so there's no train/test leakage.
✓ Safety was designed in
Confidence gating, a cooldown and duplicate suppression on every command.
✓ Simulation-first discipline
Full validation in sim before hardware — best practice, and zero physical risk.
18
Notes: The credit side: strong scholarship, a verified result, a working robotics integration, and good hygiene and safety thinking.

## Slide 16
Selected references
Wolpaw, J. R. et al. (2002). Brain–computer interfaces for communication and control. Clin. Neurophysiol., 113(6).
Pfurtscheller, G. & Lopes da Silva, F. H. (1999). Event-related EEG/MEG synchronization & desynchronization. Clin. Neurophysiol., 110(11).
Ramoser, H. et al. (2000). Optimal spatial filtering of single-trial EEG. IEEE Trans. Rehab. Eng., 8(4).
Lotte, F. et al. (2018). A review of classification algorithms for EEG-based BCIs: a 10-year update. J. Neural Eng., 15(3).
Roy, Y. et al. (2019). Deep learning-based EEG analysis: a systematic review. J. Neural Eng., 16(5).
Blankertz, B. et al. (2007). The non-invasive Berlin Brain–Computer Interface. NeuroImage, 37(2).
Abiri, R. et al. (2019). A comprehensive review of EEG-based BCI paradigms. J. Neural Eng., 16(1).
Padfield, N. et al. (2019). EEG-based BCIs using motor imagery: techniques & challenges. Sensors, 19(6).
Ang, K. K. et al. (2012). Filter Bank CSP on BCI Competition IV Datasets 2a/2b. Front. Neurosci.
Tangermann, M. et al. (2012). Review of the BCI Competition IV. Front. Neurosci., 6, 55.
Welch, P. D. (1967). Use of the FFT for estimation of power spectra. IEEE Trans. Audio Electroacoust., 15(2).
Nicolas-Alonso, L. F. & Gomez-Gil, J. (2012). Brain–computer interfaces, a review. Sensors, 12(2).
Full 20-reference IEEE list is in the project's bibliography report. Results reproduced with MNE-Python + scikit-learn.
21
Notes: Selected references; the full list is in the bibliography report. Reproduction used MNE-Python and scikit-learn.