## Slide 1
09/07/2026
Nishant shetty
End-to-End Motor Imagery BCI
Translating Biological Intent into Robotic Action

## Slide 2
1. Introduction and Motivation
Neuroscience and Signal Processing
Classification and Robot Control
Testing, Data, and Results
02
Agenda

## Slide 3: Introduction and Motivation
03

## Slide 4: Thought to Robot Motion
What the system does
It turns imagined movement into motion commands for a UR5e cobot.
End-to-end ﬂow
Brain signals are processed, classified, and converted into robot actions.
Where it runs today
In ROS and Gazebo, the robot responds to intent inside simulation.
04
INTRODUCTION AND MOTIVATION

## Slide 5: Why It Matters
A clear 4-step pipeline
Signals are captured, key patterns are extracted, then classified.
The final output is a safe actuation command for the robot.
Why it matters to everyone
It demonstrates how BCIs can guide real machines in practice.
It frames a future of accessible interaction beyond mouse and touch.
Hands-free, intent-driven control
It turns imagined movement into robot commands, without controllers.
This shows how brain signals can become direct, usable actions.
05
INTRODUCTION AND MOTIVATION

## Slide 6: Neuroscience and Signal Processing
06

## Slide 7: Motor Intent in M1
Origin of motor intent
Movement planning begins in the primary motor cortex (frontal lobe).
Different regions correspond to different parts of the body.
Neurons that scale up
Pyramidal neurons align similarly, like tiny vertical dipoles.
When many fire together, their voltages add into a larger signal.
What EEG can capture
EEG senses the summed activity across thousands of neurons at once.
This macroscopic pattern becomes the input used by our BCI pipeline.
07
NEUROSCIENCE AND SIGNAL PROCESSING

## Slide 8: Resting motor rhythms
Sensorimotor baseline
When you rest, motor areas produce steady, repeating EEG rhythms.
This “idling” pattern is the reference state for later comparisons.
Two key rhythm bands
Mu rhythm sits around 8–13 Hz and reﬂects motor-system standby.
Beta rhythm spans 13–30 Hz and is also strong during rest.
Why it matters
Imagined movement is detected as a drop from this baseline power.
08
NEUROSCIENCE AND SIGNAL PROCESSING

## Slide 9: Contralateral ERD Signal
Contralateral brain control
Left hemisphere activity typically relates to right-side intention, and vice versa.
Imagery breaks the resting pattern
When you imagine movement, the usual steady rhythm becomes less synchronized.
A measurable power drop appears
Local signal energy decreases near motor areas during imagined action.
Key clue the model learns
This event-related desynchronization (ERD) helps separate intent classes reliably.
09
NEUROSCIENCE AND SIGNAL PROCESSING

## Slide 10: Teaching biology to code
From signals to meaning
Software receives only time-series voltages, not human intention.
Learning is needed to connect patterns with imagined movement.
Supervised learning setup
We label examples by motor imagery class, then train a model.
Training teaches the system what ERD-like changes look like.
Working in real-world noise
The model must recognize intent even when signals drift and vary.
Output becomes reliable class predictions that can drive control.
10
NEUROSCIENCE AND SIGNAL PROCESSING

## Slide 11: CSP: Where activity lives
What CSP does
It learns spatial filters by comparing patterns across all EEG channels.
It re-weights electrodes so informative regions contribute more to features.
Why it helps motor imagery
It amplifies left-versus-right hemisphere differences tied to imagined movement.
It suppresses shared background activity that can mask class-specific signals.
Practical takeaway
CSP highlights where scalp activity is most useful before classification.
11
NEUROSCIENCE AND SIGNAL PROCESSING

## Slide 12: Tracking EEG Power Shifts
PSD turns EEG into a frequency map
It shows how much signal power exists at each frequency.
This makes subtle rhythm changes easier to spot than raw waves.
Welch + FFT focus on key bands
Welch’s method stabilizes estimates by averaging short time windows.
FFT reveals the spectrum, highlighting the 8–30 Hz region.
What we expect during motor imagery
A drop in power indicates ERD in mu and beta rhythms.
Those frequency features feed the classifier for intent prediction.
12
NEUROSCIENCE AND SIGNAL PROCESSING

## Slide 13: Classification and Robot Control
13

## Slide 14: SVM + Confidence Gate
Why it matters in practice
The threshold reduces twitchy switching between classes over time.
This supports safer, steadier behavior during real robot control.
Confidence-gated commands
Only send robot actions when confidence is at least 65%.
Lower-confidence outputs are treated as uncertain and ignored.
Separating intent patterns
An RBF SVM draws ﬂexible boundaries between movement-intent clusters.
This turns extracted features into a single predicted class label.
14
CLASSIFICATION AND ROBOT CONTROL

## Slide 15
Intent-to-direction mapping
LEFT_HAND and RIGHT_HAND shift the arm left or right.
FEET and TONGUE drive the end-effector front or back.
Safe default behavior
BASELINE always sends the robot back to HOME.
Robot command format
Each prediction becomes a UR5e pose command: [x, y, z, rx, ry, rz].
Pose targets are predefined so motions look smooth and repeatable.
15
CLASSIFICATION AND ROBOT CONTROL
UR5e Motion Mapping

## Slide 16: Testing, Data, and Results
16

## Slide 17: BCI Pipeline Simulation
Why we simulated
With no EEG headset available, we validated the pipeline in Python.
How we generated signals
Synthetic motor-rhythm sine waves were embedded in 25-channel noise.
What this proved
CSP, PSD, and SVM produced stable, end-to-end control outputs.
17
TESTING, DATA, AND RESULTS

## Slide 18: Real Clinical Data Input
Clinical benchmark dataset
We used Subject 1 training data from BCI Competition IV-2a.
Clean trial labeling
Embedded digital event markers split recordings into labeled imagery segments.
This produced 288 motor-imagery trials ready for model training.
Apples-to-apples comparison
Trials were exported as a 25-channel CSV matching our simulation format.
That kept preprocessing consistent for a fair simulation-versus-real test.
18
TESTING, DATA, AND RESULTS

## Slide 19: Sim vs Real EEG
Why accuracy drops in real data
ERD changes are subtle and get buried in natural variability.
Clean math vs messy biology
Simulation is smooth and predictable, so patterns stand out clearly.
Real EEG adds blinks, heartbeat, breathing, and 50 Hz power noise.
Same structure, fair comparison
Both streams use 250 Hz, 25 channels, and four motor classes.
19
TESTING, DATA, AND RESULTS

## Slide 20
Proof of concept validated
Simulation runs reliably, showing clear intent-to-motion behavior.
Confidence gating reduces uncertain commands and stabilizes control.
Next: real-world robustness
Improve performance under non-stationary clinical EEG noise and artifacts.
Retune features and models to better expose subtle ERD patterns.
End-to-end system delivered
EEG intent classification is fully linked to UR5e actuation.
ROS/Gazebo provides a complete, repeatable closed-loop demo environment.
20
TESTING, DATA, AND RESULTS
Outcome & Next Steps